## Slide 1: Single-View Refraction Tomography with Neural Fields
Anonymous CVPR Submission
Paper ID 16487
Notes: We present a novel method for tomography of refractive fields from a single viewpoint.

## Slide 2
Refractive Index η
Discrete η
η(x)
Continuous η
Notes: Refraction is the bending of light as it encounters a change in medium. When light hits this glass block, its path bends according to the difference in the
(next) Refractive Index between the air and the glass. (next)This is an example of a change in the refractive at a (next) discrete boundary. However, we are interested in (next)
recovering fields with a continuously varying refractive index. (Next) In these fields the refractive index is a continuous function of position x (Next) When rays of light travel through these fields, they curve continuously in space, rather than bending only at boundaries.
(Next)

## Slide 3
Continuous Refractive Fields
Scene Representation
Imaging Hot Air
Dark Matter Imaging
Bemana et al. 2022
Xue et al. 2014
Oguri et al. 2017
Gradient-Index Optics
Teh et al. 2022
Notes: Continuous refractive fields appear in many applications, such as (next) design of special optics, (next) detecting the shape and structure of refractive objects in scene representation, (next), and imaging refraction patterns caused by hot air or gases. (next) The application we are motivated by is weak gravitational lensing, in which massive clumps of dark matter bend the light that reaches us from faraway galaxies. Recent advances in imaging technology have made it possible to use these galaxies as a probe to measure the distribution of dark matter in the universe. Current approaches use a simple linear tomography approach similar to filtered backprojection, resulting in smearing along the line of sight; we hope to improve upon these models by modeling curved ray paths with a continuous refractive field.

## Slide 4
(exaggerated curvature)
Sensor
Image Measurements
(Refracted)
Light Sources
Notes: Refractive fields themselves are invisible, so if we want to (next) detect them we have to observe their refractive effects on light from (next) visible light sources.
In this work we focus on settings where small light sources are scattered throughout the refractive volume, much like galaxies in space (next).
Light from these light sources travels along curved paths to a sensor to form (next) a refracted image measurement. Evidence of refraction can then be found in warping and rotation of the shapes of the light sources.

## Slide 5
Light Sources
Image Measurements
(No Refraction)
Notes: Here, we show the effects of this warping on synthetic image measurements. In the top left are image measurements one would observe in the absence of a refractive field

## Slide 6
(exaggerated curvature)
Light Sources
Image Measurements
(Refracted)
Notes: And now image measurements with the effects of refraction.

## Slide 7
Forward Model
Inverse Problem
Reconstruction
?
True Refractive Field
Image
Light Sources
(x)
Notes: We are interested in solving the inverse problem of refractive field tomography. (next) Given an (next) observed refracted image from a single viewpoint, and (next) knowledge of the distribution of light sources in a scene, we wish to (next) estimate the structure of the Index of Refraction field underlying a scene.

## Slide 8
Tomography: Traditional vs. Refractive
Computed Tomography (CT):
3D Medium directly affects measured pixel intensities
Opaque medium
Refractive Tomography:
3D Medium affects ray paths from light sources
Transparent medium
Notes: Recovering the 3D distribution of a refractive field is a form of tomography. However, in traditional computed tomography, the opaque 3D medium, for example a human head, directly affects the measured pixel intensities by how much light it absorbs. On the other hand, measurements in refractive tomography only give clues about the transparent 3D structure of a refractive field by observing the refractive effect on visible light sources.

## Slide 9
Challenge #1: Nonlinear Ray Paths
Computed Tomography (CT):
Ray paths are linear, known
Linear Inverse Problem
Notes: Refractive tomography poses several challenges as compared to standard computed tomography. In standard linear computed tomography (next), a beam of X-ray radiation is aimed at a body part, and then a sensor on the other side of the beam measures how much radiation is blocked along the beam’s path. (Next) Here projection paths are known and linear in a controlled setting. This makes 3D volume recovery for CT a linear inverse problem.

## Slide 10
Challenge #1: Nonlinear Ray Paths
Refractive Tomography:
Ray paths are curved, unknown
Nonlinear Inverse Problem
Refractive medium changes ray paths
Notes: On the other hand, in refractive tomography, ray paths are both nonlinear and dependent on the structure of the unknown volume. Because the ray paths are dependent on the refractive medium, refractive tomography is a nonlinear inverse problem which can be more challenging to solve. Here you can see that for these different refractive volumes, the projection geometry of rays from the back face varies depending on the structure of the unknown refractive volume.

## Slide 11
Challenge #2: Single Viewpoint
Computed Tomography (CT):
Access to many viewpoints
Well-constrained recovery
Notes: In addition, (next) CT is done with access to many viewpoints surrounding the 3D volume, (next) making recovery well-constrained.

## Slide 12
?
?
Refractive Tomography:
Single Viewpoint
Highly Ill-posed
Challenge #2: Single Viewpoint
Notes: In (n) our problem setting, we only have measurements from a single viewpoint. Observing galaxies billions of light years away can effectively only be done from a single viewpoint which is Earth’s location. (Next) As a result, the problem is highly ill-posed. (Next)

## Slide 13
?
?
Single Viewpoint Tomography is Ill-Posed
Notes: In fact solving any tomography from a single viewpoint is highly ambiguous. (N)

## Slide 14
Single Viewpoint Tomography is Ill-Posed
Atcheson et al. 2009
Wang et al. 2022
Notes: Similar refractive tomography problems typically use multi-camera setups imaging a high frequency background through a refractive field for 3D reconstruction.

## Slide 15
?
?
Challenge #2: Single Viewpoint is Ill-Posed
Ingredient 1: Knowledge of Light Source Locations
Ingredient 2: Neural Representation
(x)
Notes: However, we are able to address this single-viewpoint limitation through a combination of two ingredients. The first ingredient is that we assume knowledge of the locations and shapes of dense point-like light sources located throughout the volume. This helps us to supervise the reconstructed volume spatially, and is motivated partially by the applications that we wish to target.

## Slide 16
?
?
Challenge #2: Single Viewpoint is Ill-Posed
Ingredient 1: Knowledge of Light Source Locations
Ingredient 2: Neural Representation
(x)
Notes: In our work, we also use a neural representation of the 3D volume, which has been shown to give a good implicit prior for a wide range of iill-posed inverse problems. We have found that using light source locations to spatially supervise refractive field recovery in addition to a neural field representation of the refractive volume can help us to overcome the ill-posedness of refractive recovery.

## Slide 17
(x)
(x)
Notes: To solve this inverse problem, we take an analysis-by-synthesis approach inspired by recent advances in neural scene representation. We use a coordinate-based neural network taking a 3D position x as input which outputs an index of refraction for that point. (next) That network then represents a predicted refractive field.

## Slide 18
Network Output
Predicted Image
Observed Image
Loss
Ray Tracing
Predicted Paths
Autograd
Autograd
Notes: Next, we solve a set of ODEs to explicitly calculate ray paths through the refractive field.. (n) The spatial steps given in these equations are determined by both the index of refraction eta and its spatial gradient. (n) This fact makes our neural field representation convenient, because it can represent a field and its spatial gradient, (next) and we can easily take gradients of both these functions with respect to its parameters for gradient descent. (n) After ray tracing to our sensor, we project light from light sources along these ray paths to synthesize a refracted image measurement.(n)This predicted image is compared with the ground truth measurements, and an image loss is backpropagated to train the weights of our neural network. We can think of this model training as optimizing the paths rays take through our field to fit the observed image measurements.(n)Therefore these ray paths are supervised locally by nearby light sources. This allows us to recover the three-dimensional structure of a refractive field despite having access to only a single viewpoint.

## Slide 19
Coordinate MLP
Refractive Field
Ray Tracing
Model Prediction
Observed Image
Image
Loss
Optimization via Gradient Descent
Notes: The full model optimization pipeline is shown here. As a summary, we solve for the weights of a neural network that defines a continuous refractive field. By ray tracing through this refractive field we can synthesize a predicted image measurement. This predicted image measurement is then compared with our actual observed image. Because every step of our pipeline is differentiable, we can optimize our model weights with this image loss using gradient descent.

## Slide 20
Ground Truth
Reconstruction
Light Sources
Indicates Sensor Direction
Notes: Using our approach we can recover (next) randomly generated refractive fields (next) given (next) single-viewpoint measurements of a dense field of light sources.(n) however, due to the ill-posedness of this problem, our method can still be susceptible to artifacts in the reconstruction.

## Slide 21
Throughout Volume
Behind Volume
Neural Field
Voxel Grid
Light Source Distribution
Measurement Type
Displacement
Behind Volume
Our Setting
30.7 dB
24.2 dB
25.8 dB
20.2 dB
20.6 dB
21.0 dB
Image
Image
Ground Truth
Reconstruction
25.3 dB
25.5 dB
25.6 dB
Voxel Grid (TV2)
Ground Truth
Notes: We compare refractive reconstruction (n) of a fuel injection volume under nine conditions: (n) three sets of measurement conditions paired with (n) three different reconstruction strategies. (n) In particular, we show that single-view refractive tomography is made possible (n) by a combination of the measurement conditions of our problem setting and the implicit regularization given by our neural field model. While other measurement conditions and models have been used successfully for reconstruction in multi-view settings, they can become susceptible to artifacts in the single-view setting.

## Slide 22
Ground Truth
50 Sources
100 Sources
250 Sources
22.2 dB
22.6 dB
25.3 dB
Light Source Sparsity
Indicates Sensor Direction
Notes: The reconstruction quality of our method is poorer if we image sparser fields of light sources, but we are still able to accurately resolve the foreground structure of a refractive field when we do so.

## Slide 23
Notes: Finally, we apply our method to image a refractive field corresponding to a realistic simulation of dark matter. Although just a first step, this result demonstrates promise in using our approach for mapping the distribution of invisible dark matter throughout the universe in the future. Going forward, we hope that our method could be refined to work in tandem with large upcoming telescopes such as the Dark Energy Survey and the Vera Rubin Observatory.