## Slide 1: BrainStack
Neuro-MoE with Functionally Guided Expert Routing for EEG-Based Language Decoding
Submission ID: 41670
April 2026

## Slide 2
1.
Introduction
Contents
2.
Methodology
3.
Experiments
4.
Conclusion

## Slide 3: We solve the problem of eeg-based neural language decoding.
For Silent speech decoding: signals are noisy and the activation pattern is spatially diverse.
To address this,
We propose BrainStack, a Neuro-MoE framework.
We introduce SS-EEG, a large-scale silent speech dataset (12 subjects, 24 words, 120+ hours).
BrainStack achieves SOTA performance (41.87%) and offers a scalable BCI solution.
Figure 1: BrainStack pipeline.
Silent-speech EEG is collected, partitioned into functional cortical regions, and processed by a CTNet global expert and multiple CNet regional experts. An adaptive routing gate integrates their representations to classify 24 silent words.
3

## Slide 4: Motivation: Why Region-Aware EEG Decoding?
EEG signals arise from over 8 billions of neurons firing in parallel across different brain regions. However, most decoding models treat the brain as a homogeneous space, ignoring functional specialization. This leads to poor generalization, overfitting to global noise, and failure to capture localized cognitive dynamics.
To build better BCI systems, we must embrace the modular, spatial nature of the brain — and design models that reflect it.
BCI Needs
Silent speech decoding requires fine-grained, region-aware modeling.
Our Insight
Treat each brain region as an expert; combine them smartly.
Problem
EEG decoding is noisy, unstable, and poorly localized.
Limitation of Prior Work
Global models ignore functional brain regions.
EEG is complex, noisy, and functionally diverse — one-size-fits-all models fall short.
Introduction

## Slide 5: Our Contributions
BrainStack introduces a functionally guided heterogeneous Neuro-MoE with regional experts, adaptive routing, and hierarchical distillation.
Introduction
Modular Architecture: BrainStack employs a heterogeneous Neuro–Mixture-of-Experts composed of one global CTNet expert and seven regional CNet experts, each aligned to a distinct functional brain region.
Adaptive Expert Routing + Hierarchical Distillation: We introduce an adaptive expert-routing gate for fusing global and regional representations, and apply KL-based top-down distillation from the global expert to supervise regional experts.
Large-Scale Dataset SS-EEG: We introduce SS-EEG, one of the largest silent speech EEG datasets — 12 subjects, 24 words, and over 120 hours of EEG recordings.

## Slide 6: Cortical Parcellation: 7 RoIs
We decompose EEG channels into 7 ROIs to enable localized decoding, expert specialization, and region-aware fusion in BrainStack.
Methodology
RoI 1 (Cyan): Prefrontal
RoI 2 (Purple): Frontal
RoI 3 (Dark Blue): Central
RoI 4 (Green): Left-Temporal
RoI 5 (Orange): Right-Temporal
RoI 6 (Yellow): Parietal
RoI 7 (Light Gray): Occipital

## Slide 7: BrainStack: architecture overview
Neuro-MoE with Functionally Guided Expert Routing for EEG-Based Language Decoding
Methodology
Modular Design
  One global CTNet expert and seven region-specific CNet experts form a heterogeneous Neuro-MoE architecture.
Parallel Regional Experts
  Region-aligned specialization enables efficient parallel computation and localized feature extraction.
Adaptive Expert Routing
  A gated routing mechanism performs task-aware integration of global and regional representations.
End-to-End Optimization
  All experts are trained jointly via a hierarchical multi-objective loss with distillation and progressive scheduling.

## Slide 8: Experts: CTNet & CNet
CTNet: Global Expert
Methodology
Full EEG input (all 122 channels)
Temporal patch embedding → Transformer encoder
Captures long-range contextual dependencies
Output: logits + transformer tokens

## Slide 9: Experts: CTNet & CNet
Methodology
Cnet：Local Expert
One expert per region (7 ROIs)
Lightweight CNN with temporal & spatial filters
Focused on localized neural activity
Output: logits + shallow features

## Slide 10: Hierarchical Multi-Objective Optimization
Motivation: To train global and regional experts effectively, we design a dynamic, multi-objective loss function that evolves with training progress.
Coordinated Expert Learning via Loss Scheduling and Hierarchical Distillation
💡 Unified Loss Objective
📈 Progress-Based Scheduling with Warm-Up
Methodology
• : Cross-entropy loss of gated fusion output
• , : Supervision loss of whole-brain and regional models, respectively
• : Knowledge distillation loss (soft label alignment)

## Slide 11: Adaptive Routing Gate
We fuse the outputs of all experts via an adaptive routing mechanism, which dynamically selects relevant experts based on input context:
A learnable gating mechanism dynamically activates the most relevant experts based on the input context.
Methodology
Expert-1:
Expert-2:
…
Expert-8:
Classification Logits
Where, is the learned projection and the MLP is the feedforward layer.
)

## Slide 12: SS-EEG: A Large-Scale Silent Speech EEG Dataset
Capturing internal speech activity across 12 participants and 24 vocabulary items
Experiment
🔬
📈 Task Design Silent articulation of 24 words across 6 categories, using a 4-phase trial protocol.
🧩 Scale & Diversity 12 subjects × 16 sessions, over 120 hours of EEG data, ~6000 trials per subject.
🧠 EEG Acquisition 128-channel system, 1000 Hz sampling, 1–45 Hz filtering, ICA artifact removal.

## Slide 13: BrainStack Achieves State-of-the-Art Performance
41.87%
8/10
1.06M
🏆 Top Accuracy
BrainStack reaches 41.87% average accuracy — highest among all models.
📊 Robust Generalization Achieves top-1 accuracy on 8 out of 10 subjects.
📉 Parameter Efficiency Only 1.06M parameters — significantly smaller than LaBraM (5.8M).
Consistently outperforms strong CNN, Transformer-based, and Large Brain Model baselines on SS-EEG
Experiment
Fig. Main experimental results (average accuracy) comparison chart clearly shows the performance improvement of BrainStack compared to existing models (such as EEGNet, TCNet, etc.).

## Slide 14: Functional Insights from BrainStack
Visualization reveals spatiotemporal dynamics and region-task relationships
🔬 2. Task-Relevant Brain Areas
Occipital and Temporal regions consistently show strong activation during silent speech.
Suggests critical involvement of visual processing and phonological representation.
🧠 1. Temporal Progression
Input × Gradient analysis reveals a progression from early occipital activity (100–300ms)
→ to broader fronto-temporal engagement (400–900ms).
Reflects visual perception → internal articulation transition.
Fig. Fusion weight distributions per region (colored by subject accuracy)
Fig. Temporal brain activation maps from attribution analysis
Experiment

## Slide 15: Additional Experiments: Cross-Subject and Public Dataset
Generalization of BrainStack across subjects and datasets is validated here.
Experiment
Table 1: Performance comparison on the SS-EEG dataset under the cross-subject setting.
Table 2: Performance comparison on the Thinking Out Loud dataset.
Cross-subject Protocol
BrainStack achieves the highest average accuracy (8.84%)
Consistent gains observed across most subjects, indicating better generalization.
Thinking Out Loud dataset
BrainStack: best accuracy 34.83
Despite the small vocabulary (4 Spanish words), BrainStack effectively captures distributed neural patterns.

## Slide 16: How Each Component Matters
Ablation study confirms the impact of fusion, architecture, and distillation
Experiment
Table.1 Ablation study on expert architecture, routing mechanism and loss design.
Adaptive routing, distillation, and heterogeneous design contribute significantly.
BrainStack achieves the best performance (41.63%) with only 1.06M parameters.

## Slide 17: Contributions and Open Challenges
🎯 Conclusion
We introduce BrainStack, a functionally guided Neuro–Mixture-of-Experts framework for EEG-based silent speech decoding.
By combining global context modeling, regional expert specialization, adaptive expert routing, and hierarchical distillation, BrainStack achieves state-of-the-art performance while remaining lightweight, modular, and interpretable.
⚠️ Limitations
Cross-subject generalization is still limited; model adaptation remains challenging.
Latency in real-time BCI inference was not optimized in this work.
🚀 Future work-1
Limited generalization across subjects and sessions
🚀 Future work-2
Further optimization for low-latency deployment in online BCI
🔥 What we solve
Bridge global & regional modelling via adaptive routing.
🛠️ What we achieve
SOTA accuracy (41.64%) on SS-EEG with only 1.06M parameters
Conclusion
BrainStack provides a robust and interpretable EEG decoding framework